## Slide 1: Spike-in Project
Carol Zhou

## Slide 2: Table of contents
Introduction
Methods
Results
R Function

## Slide 3: Introduction

## Slide 4: RNA Spike-in
An RNA transcript of known sequence.
  It was first used to calibrate variations in RNA hybridization assays.
  Now it is also adapted to be used in sequencing.
It is a quality control.
  Each sample is assigned and added a specific spike-in.
  If the highest-read spike-in matches the assigned spike-in, the sample is prepared and sequenced correctly.

## Slide 5: 01 02 Questions
What is the lower cutoff for the number of spike-in reads?
Are there any spike-in aliquots with low concentrations?
What is the upper cutoff for the read difference between spike-ins with the highest read and the second highest read?
Is there any cross-contamination of spike-ins in a batch?

## Slide 6: Methods
1606 COVID-19 (n = 1295), Dengue (n = 173), and BWH (n = 138) samples
Read per million (RPM) = highest spike-in reads / total reads * 1000000
Second-highest to highest spike-in-read ratio (SHR) = second-highest spike-in reads / highest spike-in reads
  Range: 0-1
The spike-in confirmation status was re-calculated
All analyses were done in R.

## Slide 7: Results Finding a lower cutoff for the RPM values

## Slide 8: Samples (n = 1363) vs Water (n = 168) RPM

## Slide 9: RPM Distribution
RPM Range | Percentage
1-100 | 20.45%
100-1000 | 44.46%
1000-10000 | 30.32%
10000-100000 | 4.28%
100000-1000000 | 0.49%
74.78%

## Slide 10: RPM Distribution
RPM Range | Percentage
1-100 | 20.54%
100-1000 | 44.42%
1000-10000 | 30.4%
10000-100000 | 4.24%
100000-1000000 | 0.41%
Percentile | RPM
20 | 94.28
15 | 61.85
10 | 32.56
5 | 12.41
3 | 7.24

## Slide 11: Spike-ins with 1-100 RPM
Assigned Spike-ins | Low RPM Count | Total Count | Percentage
ERCC-00023 | 24 | 27 | 88.89%
ERCC-00077 | 16 | 20 | 80.00%
ERCC-00054 | 18 | 23 | 78.26%
ERCC-00067 | 12 | 24 | 50.00%

## Slide 12: Results Finding an upper cutoff for the SHR values

## Slide 13: SHR Distribution
SHR Range | Count | Percentage
0-0.1 | 711 | 83.55%
≥ 0.1 | 140 | 16.45%
Percentile | SHR
80 | 0.05
85 | 0.16
90 | 0.43
95 | 0.63
97 | 0. 84

## Slide 14: Spike-ins with > 0.43 SHR
Sequenced Date | Virus | Count | Total Count | Percentage
2022-12-01 | Dengue | 15 | 18 | 83.33%
2023-02-13 | Dengue | 12 | 15 | 80.00%
2023-02-02 | Dengue | 13 | 21 | 61.90%
2022-12-08 | Dengue | 11 | 18 | 61.11%

## Slide 15: Summary
The lower cutoff for spike-in RPM
  12.41 – 100
  12.41 is the lowest cutoff
The upper cutoff for spike-in SHR
  0.16 – 0.43
  0.43 is the highest cutoff

## Slide 16: R Function

## Slide 17: confirm_spikein3.0.1
Description
A function used for calculating whether the expected spike-ins are confirmed and other spike-ins detected and their reads.
Usage
confirm_spikein3.0.1(spikein_dnanexus, spikein_ssss, spikein_sampleid)
Arguments
spikein_dnanexus | A count_summary.tsv file downloaded from DNAnexus
spikein_ssss | A csv file that contains information for the corresponding samples from SSSSS on Teams
spikein_sampleid | A csv file that contains only sample IDs for the corresponding samples from SSSSS on Teams

## Slide 18: Instruction
General  Current lab members folders  Carol  Spike-in Project  R

## Slide 19
Slidesgo.com
Citation
https://en.wikipedia.org/wiki/RNA_spike-in#
https://www.thermofisher.com/order/catalog/product/4456740